User Guide

8-Port 10/100Mbps+1GE Uplink Switch

Package Contents

Check the following contents of your package:

- Switch  x 1

- User Guide x1

- Power Cord  x1

- Accessories(Rack Mount Accessory Kit*2 ,Rubber Feet*4, screw*8)

If any part is lost and damaged, please contact your local agent immediately.

Introduction

8FE+1GE provides have 8* 10/100Mbps RJ45 port, 1*10/100/1000Mbps RJ45 supporting high-speed transmission of surveillance images and videos. The provides have VLAN function, Users can choose to turn on or off according to the different application environment, improve network security and suppress the network storm, easy to manage and maintain, to meet the requirements of the enterprise, community, hotel, office network and park network and access network

Hardware Description

Front Panel

The Front Panel Consists of Ethernet Ports. The LED indicators are also located on the panel.

DIP Switch

The DIP switch in located On the panel.

Default: the factory default mode, can normal communication between port 1~9.

VLAN: 1-8 port can be isolated each other but 1-8 port can connect to 9 port after open VLAN to stop broadcast storm to increase forwarding rate of frame.

Note: After change the mode, in order to the corresponding configuration take effect.the switch need to restart manually.

LED indicator

| LED | Color | Function |
| --- | --- | --- |
| PWR | Green | Off: No Power supply. Light: Indicates the switch has power. |
| LNK/ACT | Green | Off: No device is connected to the corresponding port. Light: Indicates the link through that port is successfully Blink: Indicates that the Switch is actively sending or receiving data over that port. |
| Speed | Orange | Off: Indicates the link through established at 10/100Mbps. Light: Indicates the link through established at 1000Mbps. |

Rear Panel

The rear panel of the Switch indicates an DC inlet power socket, the DC input power supply 12V/0.5A

Power socket
Connect the female connector of the power cord here, and the male connector to the DC( Direct  Current) power outlet. Please make sure the voltage of the power supply meets the requirement of the input voltage

Installation the Switch

This part describes how to install your Ethernet Switch and make connections to it. Please follow the following instructions in avoid of incorrect installation causing device damage and security threat.

- Before cleaning the switch, unplug the power plug of the switch first. Do not clean the switch with wet cloth or liquid;

- Do not place the switch near water or any damp area. Prevent water or moisture from entering the switch chassis;

- Do not place the switch on an unstable case or desk. The switch might be damaged severely in case of a fall;

- Ensure proper ventilation of the equipment room and keep the ventilation vents of the switch free of obstruction;

- Make sure that the operating voltage is the same one labeled on the switch;

- Do not open the chassis while the switch is operating or when electrical hazards are present to avoid electrical shocks.

Desktop Installation

Install the Switch on a desktop, please attach these cushioning rubber feet provided on the bottom at each corner of the Switch in case of the external vibration. Allow adequate space for ventilation between the device and the objects around it.

Wall-mounted installation

In the first two fixed screw on the wall as shown in the figure below

Aim at the two fixed hole switches, and the machine smoothly on the screw

Turn on the switch

Please connect the AC power cord into the rear of the switch and to an electrical outlet (preferably one that is grounded ). When the switch is power on, the LED indicators flash momentarily for one second, which represents a resetting of the system.The Power LED indicator turns on green.

Note: Please confirm the voltage is correct before power on, otherwise the switch will be damaged.

(The power input is:100V-240Vac, 50/60Hz.)

Specifications

| Model | 8FE+1GE |
| --- | --- |
| Standard | IEEE802.3, IEEE802.3u, IEEE802.3ab, IEEE802.3z,IEEE802.3az, IEEE802.3x |
| Network Media | 10BASE-T: UTP category 3,4,5 cable (≤100m) 100BASE-TX: UTP category 5 cable (≤100m) 1000BASE-T: UTP category 5e cable (≤100m) |
| MAC Address Table | 4K, Auto-learning, Auto-aging |
| Transfer mode | Store-and-Forward |
| Frame Forward Rate | 10Base-T: 14881pps/Port 100Base-TX: 148810pps/Port 1000Base-T/X: 1488095pps/Port |
| Switching Capacity | 3.6Gbps |
| Forwarding Rate | 2.68 Mbps |
| Packet buffer | 1.5M bit |
| Dimensions (L*W*H) | 168 *93 *32mm |
| Fan | Fanless |
| Power Input | DC:12V/0.5A |
| Temperature | Operating Temperature: 0°C ~ 40 °C (32 °F ~104°F ) Storage Temperature: -40 °C ~ 70 °C (-40 °F ~158°F ) |
| Humidity | Operating Humidity: 10% ~ 90% non-condensing Storage Humidity: 5% ~ 90% non-condensing |