User Guide

24GE(PoE)+2G SFP PoE Switch

Package Contents

Check the following contents of your package:

- PoE Switch x 1

- User Guidex1

- Power Cordx1

- Accessories(Rack Mount Accessory Kit*2 , Rubber Feet*4, screw*8)

If any part is lost and damaged, please contact your local agent immediately.

Introduction

The 24GE (PoE)+ 2G SFP switch is a non-network management PoE Ethernet switch independently developed by UNIPOE. It provides 24 10/100/1000Mbps adaptive RJ45 ports, each of which supports MDI/MDIX automatic flip and wire-speed forwarding. Two 1000Mbps SFP optical module slots. Ports 1-24 support power supply and comply with IEEE 802.3AF/AT standards. As an Ethernet power supply device, it can automatically detect and identify the devices that meet the standards and supply power to them through network cables.

Hardware Description

Front Panel

The following diagram shows the front panel of PoE Switch:

Default: The factory default mode is used when the CCTV is turned off. In this mode, it is equivalent to a common switch. Ports 1 to 26 can communicate normally.

CCTV: In this mode, ports 1 to 24 of the switch are isolated from each other, but ports 1 to 24 can communicate with ports 25/26. If this mode is enabled, ultra-long distance transmission of 250 meters is supported, which can solve the problem of long-distance transmission in network monitoring projects. It can replace optical fibers and network extenders, solve the problem of obtaining power from ultra-remote ends, and reduce the cost of engineering cabling.

VLAN: Isolation mode: In this mode, ports 1 to 24 and 25/26 on the switch are assigned an independent VLAN. Ports 1 to 24 can only communicate with ports 25 and 26. Ports 1 to 24 cannot communicate with each other. In this mode, connect ports 25/26 to the central switching device.

Note: After the Settings are changed, the PoE switch does not need to be manually restarted for the Settings to take effect (online).

LED Indicator

| LED | Color | Function |
| --- | --- | --- |
| PWR | Green | Off: No Power supply. Light: Indicates the switch has power. |
| LNK/ACT | Green | Off: No device is connected to the corresponding port. Light: Indicates the link through that port is successfully established at 10/100/1000Mbps. Blink: Indicates that the Switch is actively sending or receiving data over that port. |
| PoE | Orange | Off: No PoE powered device (PD) connected. Light: There is a PoE PD connected to be port, which supply power successfully. Blink: Indicates port abnormal power supply. |

Rear Panel

The rear panel of the PoE Switch indicates an AC inlet power socket, which accepts input power from 100 to 240V AC, 50/60Hz.

Power Socket 
This is an AC power socket, connect the negative plug of the power cord to this interface, and connect the positive plug to the AC power supply.

Grounding Column
It is located to the left of the power interface. Please use wire grounding to prevent lightning strike.

Installation the Switch

This part describes how to install your Ethernet Switch and make connections to it. Please follow the following instructions in avoid of incorrect installation causing device damage and security threat.

- Before cleaning the switch, unplug the power plug of the switch first. Do not clean the switch with wet cloth or liquid;

- Do not place the switch near water or any damp area. Prevent water or moisture from entering the switch chassis;

- Do not place the switch on an unstable case or desk. The switch might be damaged severely in case of a fall;

- Ensure proper ventilation of the equipment room and keep the ventilation vents of the switch free of obstruction;

- Make sure that the operating voltage is the same one labeled on the switch;

- Do not open the chassis while the switch is operating or when electrical hazards are present to avoid electrical shocks.

Desktop Installation

Place the bottom of the switch face up on a large enough stable table;

Tear off the attached sticky paper on the surface of the footpad and paste the footpad into the groove at the bottom of the chassis of the switch to prevent external vibration;

Carefully position the switch upright on the workbench.

Rack-mountable Installation

To check the grounding and stability of the EIA-19inch cabinet, use screws to fix mounting ears to both sides of the front panel of the switch. Place the switch on a bracket in the cabinet and move the switch along the guide rails to a proper position. Then, use screws to fix mounting ears to the guide rails at both ends of the cabinet. Ensure that the switch is securely installed on the tray in the cabinet slot. The mounting ear of the device is not used for weight bearing, it is only used for fixation. When installing devices in a cabinet, brackets (fixed on the cabinet) are provided below the device chassis to support devices.

Turn on the Switch

Connect the power cord, plug in, and turn on the power. After the switch is started, the switch automatically initializes. If all port indicators are on and off, the system is successfully reset. The power LED indicator is steady on.

Note: Please confirm the voltage is correct before power on, otherwise the switch will be damaged.

(The power input is:100V-240Vac, 50/60Hz.)

Specifications

| Model | 24GE(PoE)+2G SFP PoE Switch |
| --- | --- |
| Standard | IEEE802.3, IEEE802.3u, IEEE802.3ab, IEEE802.3z, IEEE802.3az, IEEE802.3x IEEE802.3af, IEEE802.3at |
| Network Media | 10BASE-T: UTP category 3, 4, 5 cable (≤100m) 100BASE-TX: UTP category 5 cable (≤100m) 1000BASE-T: UTP category 5e cable (≤100m) 1000BASE-X: MMF, SMF |
| MAC Address Table | 8K, Auto-learning, Auto-aging |
| Transfer mode | Store-and-Forward |
| Frame Forward Rate | 10Base-T: 14881pps/Port 100Base-TX: 148810pps/Port 1000Base-T/X: 1488095pps/Port |
| Switching Capacity | 52Gbps |
| Dimensions (L*W*H) | 440*207*44mm |
| Fan Quantity | 2 |
| Power Input | AC: 100~240V 50/60Hz |
| PoE Port | Port1~24 |
| PoE Power on RJ45 | Mode A 1/2(+) 3/6(-) |
| PoE Power Output | Voltage: 54V DC Power: 30W Max |
| PoE Power Budget | 250W | 370W(Optional) |
| Power Supply | 280W | 400W(Optional) |
| Temperature | Operating Temperature: 0°C ~ 40 °C (32 °F ~104°F ) Storage Temperature: -40 °C ~ 70 °C (-40 °F ~158°F ) |
| Humidity | Operating Humidity: 10% ~ 90% non-condensing Storage Humidity: 5% ~ 90% non-condensing |