| Electrical Specifications |
| --- |
| Item No. | AI617-2690X07i70C-SMA |
| Frequency Range | MHz | 617-698 | 698-960 | 1710-2690 |
| Gain | dBi | 3 | 3 | 4 |
| Polarization |  | ±45° |
| Beam width | Horizontal | deg | 80 | 70 | 65 |
|  | Vertical |  | 70 | 70 | 60 |
| Front-To-Back Ratio | dB | ≥10 | ≥15 |
| VSWR |  | ≤3.0 | ≤2.0 |
| Efficiency | % | ≥50 |
| Input Power per Port, maximum | watts | 50 |
| Mechanical Specifications |
| Dimensions, HxWxD | mm | 308x190x82 |
| Weight, without Mounting Kit | kg | 1.2 |
| Radome Material and Color |  | ABS, White, RAL9003 |
| Mounting hardware | mm | φ35～φ50 |
| Connector Type and Location |  | SMA-male×2 |
| Cable type and length |  | RG58 ,L=5000mm |
| Operational Temperature | oC | -55 to +60 |
| Operational Humidity | % | < 95 |

Radiation Patterns

Drawing：

Packing：

# Text boxes

Whatsapp /Skype:+86 17749711795 Wechat:17749711795

Email: Cathy@zxsignal.com Website: www.zxsignal.com

Whatsapp /Skype:+86 17749711795 Wechat:17749711795

Email: Cathy@zxsignal.com Website: www.zxsignal.com